## Slide 1
DRIFT
cognitive focus tracker for deep work
when you stop thinking, your pod knows
Clive Rafiq · StarkHacks 2026 · Microsoft AI & Automation + Espressif Smart Home

## Slide 2
DRIFT
2 / 10
You drift more than you think.
Attention collapses quietly — minutes before you notice the tab you drifted into.
40%
of the workday
lost to shallow task-switching that never gets logged.
0
focus apps today
measure actual attention. They measure time in a window.
23m
to reset after a slip
— the cost of a single distraction, before your brain notices.

## Slide 3
DRIFT
3 / 10
What Drift does
Drift passively measures your attention in real time, fuses it with a hardware pod on your desk,
and pokes you when you slip.
TYPING
GAZE
EXPRESSION
ENVIRONMENT
Four live signal streams, continuously fused into a single Focus number.

## Slide 4
DRIFT
4 / 10
How the signal flows
Three independent sensors → one scoring engine → two output surfaces.
Keyboard
keydown events
WPM · pauses · backspace
Webcam
MediaPipe 468pt
gaze · blink · expression
Hardware pod
ESP32-S3 USB
noise · ambient light
FUSION ENGINE
state machine
personal baseline
state-weighted mean
fatigue trajectory
focus · fatigue
Browser UI
score cards · timeline · prompts
Pod feedback
OLED mirror · piezo nag-loop
all inference local · no server · no cloud · no WiFi

## Slide 5
DRIFT
5 / 10
The pod
Desk hardware in the feedback loop, not just a display.
ESP32-S3
KY-037
mic
LDR
OLED
piezo
buzzer
USB-C <-> Chrome (WebSerial)
DATA: <noise>,<light>
streamed every 500 ms, 0–4095 each
FOCUS: 0–100
browser → pod; OLED mirrors live score
BUZZ: <ms>
pulses when gaze drifts or fatigue climbs
PING / PONG
8-second watchdog detects a silent pod

## Slide 6
DRIFT
6 / 10
Same signal, different meaning
"Not typing" means thinking if your eyes are on the screen, drifting if they're off it.
USER STATE | TYPING SPEED | TYPING CONSISTENCY | GAZE | EXPRESSION | NOISE | LIGHT
Active typing | 0.25 | 0.25 | 0.30 | 0.10 | 0.05 | 0.05
Thinking pause | — | — | 0.60 | 0.25 | 0.10 | 0.05
Reading | — | — | 0.55 | 0.30 | 0.10 | 0.05
Distracted | — | — | 0.70 | 0.15 | 0.10 | 0.05
Fatigued drift | 0.15 | 0.15 | 0.20 | 0.40 | 0.05 | 0.05
Unknown | 0.20 | 0.20 | 0.40 | 0.10 | 0.05 | 0.05
Six sub-scores · six states · weights shift in real time as the state machine flips.

## Slide 7
DRIFT
7 / 10
Fatigue is a delta, not a snapshot
A slow typer isn't fatigued. Someone whose WPM fell 25% against their own baseline is.
Your session baseline
45 seconds to lock in WPM, blink rate, eye-aspect ratio,
and head pose — averaged across live samples.
Frozen once the window closes; every later sample is
compared against that personal snapshot.
Duration ramp: a 20% WPM drop at 10 min is noise —
at 50 min it's a real signal.
Fatigue = weighted delta
WPM drop
0.30
Backspace surge
0.20
Blink anomaly (U)
0.20
Lid droop (EAR)
0.20
Head-pitch drift
0.10
Low blink rates are weighted 1.5× — microsleep-adjacent staring is the dangerous direction.

## Slide 8
DRIFT
8 / 10
Why Drift is different
Four design decisions separate Drift from a Pomodoro timer or a webcam proctor.
01
Privacy-first
Webcam frames never leave the browser. The pod has no WiFi. MediaPipe runs locally.
02
Personalized
Your baseline locks in the first 30–45 seconds. Every delta is measured against YOU.
03
Context-aware
A state machine reclassifies pauses: thinking vs. reading vs. drifting vs. fatigued.
04
Closed-loop
The pod buzzes back. Hardware is part of the feedback — not just a score display.

## Slide 9
DRIFT
9 / 10
Stack
Everything is off-the-shelf — the value is in the fusion.
FRONT END
React 18 + Vite + Tailwind 4
recharts for the session timeline
VISION
MediaPipe FaceMesh
468 landmarks · EAR blink · yaw gaze
BRIDGE
WebSerial API
Chromium-only, zero drivers, zero servers
FIRMWARE
Arduino / ESP32-S3 C++
KY-037 · LDR · SSD1306 · piezo buzzer
~1,500 lines across 9 hooks and 3 components · runs on any ESP32-S3 dev board

## Slide 10
Thank you.
Eyes on your eyes, so your work stays on your work.
TRY IT
Live on the demo laptop →
BUILT FOR
StarkHacks 2026
CONTACT
clive.rafiq@gmail.com
DRIFT